## Slide 1: Lab 3 Quiz Solution Guide
EE 306 Microprocessors

## Slide 2: Addressing modes EA: Effective Address, Rb: Base address pointer, Rd: Destination
STR Rd, [Rb, index] EA=[Rb] + index Rb is NOT updated.
STR Rd, [Rb, index]! EA=[Rb] + index Rb becomes Rb + index.
Example: Let R0 content be 128 and R1 be 64
STR Rd, [R0, 100] EA=128 + 100 = 228 R0 is still 128.
STR Rd, [R0, R1] EA=128+64 = 192 R0 is still 128.
STR Rd, [R0, 100]! EA=128+100 = 228 R0 becomes 228.
STR Rd, [R0, R1]! EA=128+64 = 192 R0 becomes 192.
STR Rd, [R0, R1, LSL #1] EA=128+64*2 = 256.
STR Rd, [R0, R1, LSR #1] EA=128+64/2 = 160.

## Slide 3: Addressing modes EA: Effective Address, Rb: Base address pointer, Rd: Destination
STR Rd, [Rb], index EA=[Rb] Rb becomes Rb + index.
Example: Let R0 content be 128 and R1 be 64
STR Rd, [R0], 100 EA=128 R0 becomes 228.
STR Rd, [R0], R1 EA=128 R0 becomes = 192
STR Rd, [R0], R1, LSL #1 EA=128 R0 becomes 256.
STR Rd, [R0], R1, LSR #1 EA=128 R0 becomes 160.

## Slide 4: Rotate
F | 0 | 0 | 0 | 0 | 0 | 0 | 2
4 bits make one hexadecimal character.
Rotating by 4 bits mean rotating one hexadecimal character.
Rotate to right by 4 bits:
Shift everything towards right then bring the rightmost 4 bits
back to the leftmost side.
F | 0 | 0 | 0 | 0 | 0 | 0 | 2
2
2 | F | 0 | 0 | 0 | 0 | 0 | 0

## Slide 5: Shift
F | 0 | 0 | 0 | 0 | 0 | 0 | 2
Logic shift means fill all gaps with zeros
Arithmetic shift copies the sign.
Shit the number towards right by 4 bits
What is the sign of this number? 0xF = 0b1111. It is 1.
So, fill with ones.
F | 0 | 0 | 0 | 0 | 0 | 0 | 2
F
F | F | 0 | 0 | 0 | 0 | 0 | 0
ASR R2, R1, #4
F | 0 | 0 | 0 | 0 | 0 | 0 | 2
Shit the number towards right by 4 bits
So, fill with zeros.
F | 0 | 0 | 0 | 0 | 0 | 0 | 2
0
0 | F | 0 | 0 | 0 | 0 | 0 | 0
LSR R2, R1, #4